- Architecture Tour for Operating Systems
  - Fetch-Decode-Execute Loop
    - View the computer as a large general purpose calculator
      - Want to program it for multiple functions
    - All Von Neumann computers follow the same loop
      - Fetch an instruction from memory
      - Decode the instruction to figure out what to do
      - Execute the instruction and store the result
    - Instructions are not complicated
      - ie: add the value of a memory cell by 1
  - The Program Counter
    - Where is the next instruction held in the machine? (It's in here, spoiler)
    - A simple memory cell in the CPU, known as the “program counter” (or simply the PC), contains the address of the next instruction
      - Special purpose memory in the CPU and all devices are called registers
    - Naive fetch cycle: increment the PC by the instruction length after each execute
      - Assumes all instructions are the same length
  - Memory Indirection
    - How can we access array elements efficiently if all we can do is name a cell?
      - Modify the operand to allow for fetching an operand “through” a memory location
        - Ex: Load[5], 2 means fetch the contents of the cell whose address is in cell 5 and put it into cell 2
      - This is known as indirection
        - Fetch the contents of the cell pointed to by the cell in the opcode
      - Steal an operand bit to signify if an indirection is desired
  - Conditionals and Looping
    - primitive computers only follow linear instructions
    - Breakthrough in early computing was the addition of branching conditionals
      - These instructions modify the program counter
    - Conditional Instructions
      - If the content of this cell is [positive, not zero, whatever], then execute the instruction (or not)
    - Branch Instructions
      - If the content of this cell is[zero, nonzero, etc], set the PC to this location
      - Jump is an unconditional branch
  - Registers
    - Architecture Rule: large memories are slow, small ones are fast
      - But everyone wants more of it
    - Solution: put small amount of memory in the CPU for faster operation
      - Most programs work only on small chunks of memory in a given time period, this is known as locality
      - If we cache the contents of a small number of memory cells in the CPU memory, we might be able to execute many instructions before having to access memory
    - Small memory in CPU named separately in the instructions from the main memory
      - Small memory in CPU = registers, large memory = main memory
    - Most CPUs have 16-32 general purpose registers
      - All of these look the “same”, they're a combo of operators, operands and destinations
    - Only memory operations possible in register only machines are load from and store in memory
    - Operations 100-1000 times faster when operands are in registers compared to when they are in memory
    - Save instruction space as well
      - Only address 16-32 registers, not a GB of memory
  - Abstracting the Machine
    - Bare hardware provides a computation device
    - How do we share this expensive piece of equipment between multiple users?
      - Sign up during certain hours?
      - Give the program to an operator?
        - Run it → give you results
    - Duh, the Operating System!
      - Need hardware support to “virtualize” machine
  - Architecture Features for the OS
    - What are some mechanisms that hardware designers add to allow OS designers to abstract the basic machine in software?
      - Processor modes
      - Exceptions
      - Traps
      - Interrupts
    - These require modifications to the basic fetch-decode-execture cycle in hardware
  - Processor Modes
    - OS code is stored in memory (von neumann model)
      - What if a user program modifies this OS code or data?
    - Modes of Operation
      - Instructions can be executed in user mode or system mode
    - Special register holds what mode the CPU is in
    - Certain instructions can only be executed when in system mode
    - Likewise, certain memory locations can only be written to when in system mode
      - Only OS code is executed in system mode
      - Only OS can modify it's memory
      - The mode register can only be modified in system mode
  - How can we protect the OS from users?
    - All addresses <100 are reserved for OS use
    - Mode register provided
      - zero = sys = cpu is executing the OS (in sys mode)
      - one = usr = cpu is executing in user mode
    - Hardware does this check
      - On every fetch, if the mode bit is user, and the instruction address is less than 100 don't execute the instruction
      - When accessing operands, if the mode bit is USR and the operand address is less than 100, do not execute the instruction
      - Mode register can only be set if mode is SYS
  - Exceptions
    - What happens when a user program tries to access memory holding the operating system code or data?
    - An exception occurs when the CPU encounters an instruction that cannot be executed
      - Need a modified fde loop to jump to a known location in the OS when an exception happens
    - Different errors jump to different places in the OS (vectored)
  - Access Violations
    - Notice both instruction fetch from memory and data access must be checked
    - Execute phase must check both operands
    - Execute phase must check again when performing an indirect load
    - This is a very primitive memory protection scheme
  - Recovering from Exceptions
    - The OS can figure out what caused the exception from the entry point
      - How can it figure out where in the user program the problem is?
    - Solution: another register, the Program Counter
      - When an exception occurs, save the current PC to PC' before loading the PC with a new value
      - OS can examine the PC' and perform some recovery action
        - Stop user program and print error message, error at address PC'
        - Run a debugger
  - Traps
    - How does a user program legitimately access OS services?
    - A trap is a special instruction that forces the PC to a known address and sets the mode into system mode
    - Unlike exceptions traps carry some arguments to the OS
      - Foundation of the system call
    - How does the OS know which service the user program wants to invoke on a trap?
      - User program passes to the OS a number that encodes which OS service is desired
    - Most CPU's have a convention for passing the trap ID in a set of registers
  - Returning from a Trap
    - How do we get back into user mode and the user's code after a trap?
      - Use two instructions?
        - Set mode register = 1 then set the PC?
          - After the mode bit is set to 1 we get an exception
        - Set the PC then the mode bit?
          - Jump to “user-land” then in kernel mode
      - Most machines have a return from exception instruction
        - A single hardware instruction that can:
          - Set the PC to PC', and set the mode bit to user mode
        - Traps and exceptions use the same mechanism (RTE)
  - Interrupts
    - How can we force the CPU back into system mode if the user program is off computing something?
    - An interrupt is an external event that causes the CPU to jump to a known address
  - Entry Points
    - Entry points are a jump to some code block in the OS
    - All real OS's have a set of entry points for exceptions, traps, and interrupts
      - Sometimes they are combined and software has to figure out what happened
  - Saving and Restoring Context
    - When an entry to the OS happens, we want to start executing the correct routine (handler) then return to the user program so it can continue normal execution
      - Can't just start using the registers in the OS
    - Solution: save/restore the user context
      - Use the OS memory to save all the CPU state
      - Before returning to user, reload all the registers and execute a return from exception instruction
  - Input/Output
    - How can humans get at the data? How do we load programs? What happens if I turn the machine off? Can I send the data to another machine?
    - Solution: add devices to perform these tasks
      - Keyboards, mice, graphics cards, disk drives, network cards
  - Simple I/O Example: A Network Card
    - Has 2 registers
      - A store into the “transmit” register sends the byte over the wire
      - A load from the “receive” register reads the last byte that was read from the wire
    - How does the CPU access these registers?
      - Map them into address space!
        - An instruction the accesses memory cell 98 actually accesses the transmit register instead of memory, an instruction that accesses memory cell 99 actually accesses the receive register
        - These registers are said to be memory mapped
  - Why memory-mapped registers?
    - “Stealing” memory space for device registers has two functions
      - Allows protection: only OS can access the device
        - User programs must trap into the OS to access IO devices because of the normal protection mechanisms in the processor
      - OS can control devices and move data to/from devices using regular load and store instructions
        - No changes to instruction set required
        - This is known as programmed IO
  - Status Registers
    - How does the OS know if something new has arrived? How does it know when the last byte was submitted so it can send another one?
    - A status register holds the state of the last IO operation
      - Our sample network card has 1 status register
        - To transmit, OS writes a byte into the TX register (transmit register) and sets bit 0 of the status register to 1. When successfully transmitted, the 0 bit of the status register is set back to 0
        - When the card receives a byte, it puts the byte in the RX register (receive register) and sets bit 1 of the status register to 1. After the OS has read the data, the 1 bit of the status register is set back to 0.
  - Interrupt driven IO
    - Polling can waste CPU cycles
      - On transmit, CPU slows to speed of the device
      - Can't block on receive, so tie polling to clock, but it's wasted if no RX data
    - Use interrupts to avoid wasting time!
      - When network has data to receive, signal an interrupt
      - When data is done transmitting, signal an interrupt
  - Polling vs Interrupts
    - Why poll at all?
      - Interrupts have a high overhead
        - Stop processor, figure out what caused interrupt, save user state, process request
      - Key factor is frequency of IO vs interrupt overhead
  - Direct Memory Access (DMA)
    - Problem with programmed IO, CPU must load/store all the data from/into device registers
      - Data is probably in memory anyways!
    - Solution: more hardware to allow the device to read and write memory just like the CPU
      - Base + bound or base+count registers in the device
      - Set base + count register
      - Set the start transmit register
      - IO device reads memory from base
      - Interrupts when done
  - PIO vs DMA
    - Lower overhead for PIO in comparison to DMA
      - PIO is a check against the status register, then send or receive
      - DMA must set up base, count, start transfer take an interrupt
    - DMA is more efficient at moving data
      - PIO ties up CPU for entire length of the transfer
    - Size of the transfer is the key factor in when to use PIO vs DMA
  - IO Design Space (Recap)
    - Polling vs Interrupts
      - How does the device notify the processor an event happened?
        - Polling: device is passive, CPU must read/write a register
        - Interrupt: device signals CPU via an interrupt
    - Programmed IO vs DMA
      - How does the device send and receive data?
        - PIO: CPU must use load/store into the device
        - DMA: Device reads and writes memory
  - How to boot?
    - How does a machine start the operating system?
      - Process of starting the OS is called booting
    - Sequence of hardware+software events form the boot protocol
    - Boot protocol in modern machines is a 3 stage process
      - CPU starts executing from a fixed address
      - Firmware loads the boot loader
      - Boot loader loads the OS
  - Boot Protocol
    - CPU is hardwired to start executing from a given address in memory
      - Memory address is typically mapped to a solid state persistent memory (ROM, EPROM, Flash etc)
    - Persistent memory contains the boot code
      - This software is known as firmware
      - On x86 the starting address corresponds to the BIOS (basic input output system) boot entry point
      - This code reads 1 block from the disk drive. This block is loaded and then executed, the program is the boot loader
    - The boot loader then loads the rest of the operating system from disk, at this point the OS is still not running
      - Boot loader can know about multiple OS's, can know about multiple versions of same OS
  - Why have a Boot Protocol?
    - Separate the OS from the hardware instead of storing in persistent memory
      - Multiple OS's or different versions of same OS
    - Want to boot from different devices (security via a network boot)
    - OS is large, wouldn't work as firmware
  - Multi CPU Chip Multiprocessors
    - SMP (simple scheme): more than one CPU on the same bus
    - Memory is shared amount CPU's – cache coherence between LLCs
    - Bus contention increases – does not scale
    - Alternative (non-bus) system interconnect – complex and expensive
    - SMPs naturally support single-image operating systems
  - CC-NUMA Multiprocessors
    - Non-uniform access to different memories
    - Hardware allows remote memory accesses and maintains cache coherence
    - Scalable interconnect and, more scalable than bus-based UMA systems
    - Also naturally supports single-image operating systems
    - Complex hardware coherence protocols
  - Multicomputers
    - Network of computers: share-nothing (cheap)
    - Distributed resources: difficult to program
      - Message passing, distributed file system
    - Challenge: build efficient global abstraction in software